## Slide 1: Humidity Sensor April 2014

## Slide 2: Outline
An Humidity introduction
TI Humidity solution
Humidity Sensing application
Humidity sensing competition
HDC1000/HDC1050
Package description
Roadmap
EVM Description
EVM GUI description
Summary

## Slide 3: An Introduction to Humidity
What’s RELATIVE HUMIDITY?
  Ratio (at a fixed temperature) between actual water vapor and saturation water vapor expressed as percentage (saturation is the max water vapor)
      Saturation  water vapor start to condense
  %RH change significantly with the temperature
    +1°C variation  -4%RH relative humidity
    Precise temperature measurement is needed
Dew Point - Temperature at which moisture condense (air is saturated)
  to identify this temperature a precise temperature sensor is needed.
  Avoiding the condensation is important is several application as automatic windshield defog, industrial process ect.
  Combination of accurate humidity and temperature sensor is needed
Water
Water Vapor

## Slide 4: TI’s Humidity Sensing Solution
Fringe capacitance changes as water is absorbed/desorbed by polyimide
Readout electronics converts cap value variation into RH value
Sensor is integrated using standard technology
(sensor cross-section)
Polyimide
Metal
Metal
Working Principles
Upper metal layer
Implementation
Polyimide
Block diagram

## Slide 5: Humidity Sensing Applications
HDD
Adjust physical parameters to maximize performance (e.g., head height)
Mobile devices
Remote weather station, sports/exercise, health, Humidifier
White goods
Washer, microwave, dryer, dishwasher, refrigerator
HVAC
Building control
Printers
Modify print speed
Automotive
HVAC, fog detection

## Slide 6: HDC Competition
Company | TI | COMP A | COMP B | COMP C | COMP D
Size (mm) | 1.59 x 2.04 3x3 | 3x3 | 2x2 | 3x3 | 2x2
Package | WCSP-8 / DFN-6 | DFN-6 | DFN-4 | DFN-6 | LGA-6
VDD (V) | 2.7 ÷ 5.5 | 2.1 ÷ 3.6 | 1.62 ÷ 1.98 | 1.9 ÷ 3.6 | 1.71 ÷ 3.6
Resolution Max (%RH) | 14-bit | 12-bit | 12-bit | 12-bit | 16-bit
Isupply @ 1/s ( Hum+Temp 11bit resolution) (uA) | 1.1 | 6.5 | 4.8 | 1.1 | 2.0
Accuracy (%RH) | ±2 | ±3 // ±2 // ±1.8 | ±5 | ±4 // ±3 | ±3
Temp acc (degC) | ±0.5 | ±0.45 | ±0.5 | ±0.4 | ±1
Operating Range (%RH) | 0 – 100 | 0 – 100 | 0 – 100 | 0 – 100 | 0 – 100
Interface | I2C | SPI / I2C / PWM | I2C | I2C | I2C/SPI
Operating Range (degC) | -40 to +125 | -40 to +125 | -30 to +100 | -40 to +125 | -25 to +85
TI Values
Smallest Size with WCSP 2. Lowest Power 3. High accuracy

## Slide 7: HDC1000/1050 Humidity & Temperature Sensor
Completely integrated humidity and temperature IC provides guaranteed performance
Fully calibrated sensor enables quick time-to-market
Very low power consumption
Small package size supports compact designs
Applications
HVAC
White goods (dryer, fridge, microwave, dishwasher)
Printers
Handheld Meters
Camera Defog
Smart Thermostats and Room Monitors
Medical Devices
Features
Benefits
HDC1000 Samples : now – RTM July
HDC1050 Samples: Q2’14– RTM November
Relative Humidity Range 0% to 100%
Humidity Accuracy ±2%
Typical Drift < 0.5%/yr
Supply Current (Measuring) 180uA
Avg Supply Current (@1sps) 1.1uA
Temperature Accuracy ±0.5ºC
Temperature Range (Operating) -20ºC to +85ºC
Temperature Range (Functional) -40ºC to +125ºC
Operating Voltage 3V to 5V
Package
  8 pin WCSP HDC1000 (1.59mm x 2.04mm)
  6 pin DFN HDC1050 (3mm x 3mm)
CDC
I2C
Calibration & Temp Compensation
S-D
ADC
Temp
C2V
EEPROM
Polyimide

## Slide 8: HDC1000 Humidity accuracy @ 25 °C
* Typical value
Limit
Spec
Limit
Spec

## Slide 9: HDC1000 Humidity accuracy over temperate
Main competitor
performances
* Typical value

## Slide 10: Packages Descriptions
HDC1000: 8-WCSP
HDC1050 – 6-DFN
3.00
3.00

## Slide 11: Humidity Sensing Roadmap Sample Dates
Legend
2014
2015
HVAC
White Goods Printers
RH Accuracy
Low (+/-5%)
High (+/-2%)
Special
Application
HDD
Automotive
HDC1000
2.7-5.5V
WCSP-8
HDC1050
2.7-5.5V
DFN-6
HDC1010
2.7-5.5V
WCSP-8
HDC2010
1.8V
WCSP-8
HDC1000-Q
2.7-5.5V
WCSP-8
Definition
Sampling
Planned
Concept
Down-spec
New 1.8-V core
HDC2000
1.8V
WCSP 8
Down-Spec
Mobile Devices
Battery application
HDC2050
1.8V
DFN-6

## Slide 12: HDC1000 EVM
EVM HDC1000
  EVM is pre-cut to enable the customer to separate the HDC1000 from the main board and better place the sensor using a simple 5 wires connection
1st Pre-cut
2nd Pre-cut

## Slide 13: EVM GUI interface
Humidity and temperature
µC Sampling Rate
File data log
Devices Settings

## Slide 14: Summary
Humidity Sensor is used in several application
  Printer, Defog, HVAC, Dryer, Refrigerator, Weather Station, humidifier, etc.
HDC1000/HDC1050
  High accuracy, extremely low power consumption and small footprint
    HDC1000: RTM July 2014
    HDC1050: RTM November 2014
EVM and GUI
  HDC1000 available
  HDC1050 available Q2’14

## Slide 15: Thanks